## Slide 1: Autonomous Control of Air-Launched Fixed-Wing Drone Swarm
Culminating Experience Project in the Pursuit of Mechanical Engineering Master’s Degree
Alex Springer, June 2021 - May 2024

## Slide 2: Project Definition and Overview
Air-Launched Drone Swarms
Independent Non-Linear Agent Control System
User-Specified Commands:
  Fly-Over Waypoints
  Drone trajectories
Agents Tracked by C2 Aircraft
Agents Autonomously Assigned to User Commands
Use-Case: Search and Rescue in Mountainous Terrain

## Slide 3: Control System Hierarchy
Agent States Continuously Estimated
User Input of Fly-Over Waypoint (applications: search & rescue, surveillance, package drop)
Latitude, Longitude, Altitude, Groundspeed
Cost Estimated for Each Agent: Distance, Altitude, Heading, and Groundspeed all considered
Individual Agent Controller
Agent-Waypoint Assignment
Linear Hungarian Assignment Algorithm Used to Assign Agents and Minimize Overall Cost
Proportional Controller Converts Waypoint Assignments to Controller Inputs At Each Time Step
Non-Linear Navigation Controller to Command Airspeed, Heading, and Rate of Climb
Each Agent Tracked by Command & Control Aircraft
Agent Position, Velocity, and Acceleration Estimated by Random Finite-Set Based Filter
User Input

## Slide 4: Fixed-Wing Aircraft Non-Linear Guidance System (FANGS)
Individual Agent Flight Controller

## Slide 5: The Underlying Controller for Each UAS Agent
Based on Nonlinear Aircraft-Performance Simulation by Dr. John Schierman in his Modern Flight Dynamics textbook
Rigid fixed-wing aircraft operating in steady wind
Uses a default state estimator with ideal equations of motion
  User can provide a state solution at any time step; any unprovided state variables are estimated using the default ideal estimator
Input: desired flight profile
  Velocity, rate of climb, and heading

## Slide 6: Simulation Setup
Drones modelled loosely from a C-130 fixed-wing aircraft
  Long flight-time and/or range
  Heavy payload (cameras, telemetry, first-aid package drop, etc.)
Each drone launched from a C2 helicopter
Flight controller in operation 150 feet after launch
  Assume wings deploy during first 150 feet
  After 150 feet, assumed 50 kts airspeed with no ascent or descent
8 drones launched ~5 seconds apart

## Slide 7: Ideal EOM: Governing Equations
Translational equations of motion for a vehicle with propulsive thrust aligned with the fuselage x-axis:
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 8: Ideal EOM: Simplifying Assumptions
Steady level flight or coordinated turns (sideslip and side force are zero)
Assume sufficiently small angles of attack such that
The governing equations become
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 9: Ideal EOM: Engine and Airframe Responses
First-Order Differential Equations Used to Approximate the Engine and Airframe Responses
Limits imposed on the responses
Time constants , , set to 2.0, 0.5, and 1.0, respectively, in simulation
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 10: Ideal EOM: Aerodynamic Responses
The model used in the ideal equations of motion for aerodynamic lift and drag
where, , , and
Note: FANGS is designed to operate within the presence of wind, where
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 11: Ideal EOM: Angle of Attack and Drag
Invert the prior equations to find the inferred Angle of Attack and Drag given a Lift command
where , , and
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 12: Guidance Laws – Transfer Functions
Inputs: Commanded Velocity , Rate of Climb , and Heading
Outputs: Commanded Thrust , Lift , and Bank Angle
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 13: Guidance Laws - ODEs
Convert the transfer functions to ODEs to be programmed in Python 3 and solved using scipy.integrate.solve_ivp with the RK45 method:
where , , and
Reference: Modern Flight Dynamics by Dr. John Schierman

## Slide 14: Implementation (Python 3)
FANGS.py
  Create an object of class GuidanceSystem
    Initialization inputs:
      vehicle: Object of type FixedWingVehicle
      TF_constants: Dictionary of PI Controller transfer function coefficients ()
      InitialConditions: Dictionary of initial conditions
    User-Accessible Functions:
      setCommandTrajectory()
      setFlyoverCommand()
      getGuidanceCommands()
      updateSystemState()

## Slide 15: Implementation (Python 3), continued
After initialization, the drone is commanded to fly at initial conditions.
The user may give any drone a command of either:
  Trajectory
    The user will supply a desired airspeed, heading, and rate of climb.
  Flyover
    The user will supply a desired waypoint, altitude, and groundspeed.
Alternatively, the user may give the swarm a list of Flyover commands
  See ATAMS section for more.

## Slide 16: User Commands: Trajectory
User may request a trajectory command at any time:
  Velocity , Rate of Climb , and Heading
  Use setCommandTrajectory()
Guidance Laws calculated when getGuidanceCommands() is called
  Run this each time step
Use-Case: Loiter, Send-To-Home

## Slide 17: User Commands: Flyover
The user may request a flyover command at any time:
  Groundspeed (feet/sec), Altitude (ft, MSL), Waypoint (latitude, longitude)
  Use setCommandFlyover()
An internal flag will note that a flyover has been requested
At each timestep, when getGuidanceCommands() is run, FANGS will internally convert flyover commands to trajectory commands for the aircraft guidance logic
  Proportional Controller: see next slide

## Slide 18: User Commands: Flyover, continued
Correct aircraft altitude before adjusting velocity
  Calculate required glideslope to reach command altitude
    if :
    elseif :
    else:

## Slide 19: User Commands: Flyover, continued
Once altitude is stabilized, fly as fast as possible until within 2 miles of the flyover point
if :
    if distance from target 2 miles:
    velocity = maximum allowable velocity - 15
    else:
    velocity =

## Slide 20: User Commands: Flyover, continued
While changing velocity and altitude, continually adjust heading to intercept flyover point
    heading = bearing between(current latitude/longitude, target latitude/longitude)
If the aircraft is within 300 feet of the target, “let go” of the flyover waypoint and switch to a trajectory controller holding the current flight path for intercept.
  Aircraft will maintain this flight path until the user specifies a new trajectory or flyover command

## Slide 21: Example Simulation – Single Agent
Initial Conditions
  Airspeed = 50 knots
  Altitude = 7000 feet above mean sea level
  Ascent = 0 degrees
  Heading = 0 degrees (North)
  (Latitude, Longitude) = (36.2434, -112.2822) degrees
  Weight = 80 pounds
  Wind = 15 knots east

## Slide 22: Example Simulation – Single Agent
Drone Parameters
  Max speed = 75 knots
  Min speed = 25 knots
  = (2.0, 0.5, 1.0)
  Max thrust = 45 pounds
  Max = 0.26
  Max bank angle = 45 degrees
  = 0.05
  = 0.5 radians
  = -0.1 degrees
  Wing area = 8 square feet
  Aspect ratio = 12
  Wing efficiency factor = 0.8

## Slide 23: Example Simulation – Single Agent
Controller Transfer Function Gains

## Slide 24: Example Simulation – Inputs
Initial conditions: 50 knots, level flight, North heading (0o)
  15 knot wind out of the west
After 120 seconds, command trajectory: 95 knots, 6-degree ascent, West heading (270o)
After 600 seconds, command flyover: 50 knots, 11000 feet MSL, (36.530367, -112.057600)
After 1800 seconds, command flyover: 50 knots, 7700 feet MSL, (36.449291, -112.399009)
Simulate 45 total minutes of flight time

## Slide 25: Results

## Slide 26: Example Simulation Results, Altitude and Airspeed
Dives commanded to match flyover altitudes
Airspeed response overshoot before settling due to proportional control

## Slide 27: Example Simulation Results, Thrust, Drag, and Flight Path Angle

## Slide 28: Agent Tracking and Assignment Management System (ATAMS)
Agent-Waypoint Assignment

## Slide 29: Target Assignments – Cost
Cost value assigned to each target-agent assignment
  Each calculation uses a weighting that can be user-defined
    : Weighting of Distance Cost
    : Weighting of Altitude Cost
    : Weighting of Velocity Cost
    : Weighting of Heading Cost
Calculate the cost of each possible agent-target assignment
  Ex: If 8 active agents and 4 assignments, 32 total cost calculations

## Slide 30: Target Assignments – Cost, Continued
Distance Cost:
  Simply multiply the distance between the agent and the target by
Heading Cost:
  Simply multiply the heading change required to intercept the target by
Altitude Cost:
  Multiply the required change in altitude by
  If the required altitude is lower than the current agent altitude, multiply the cost by 0.75
    It is cheaper to lower an agent’s altitude than raise it
Velocity Cost:
  Simply multiply the velocity change required by
Total Assignment Cost: Sum the Distance, Heading, Altitude, and Velocity cost

## Slide 31: Target Assignments – Cost Matrix
Cost Matrix calculated using Hungarian Algorithm
  Use Python 3 scipy package scipy.optimize.linear_sum_assignment
  Returns cost matrix of n targets to m agents
Targets assigned by Cost Matrix

## Slide 32: Target Assignments - Example
Eight active airborne agents
  Each defined using parameters in Single Agent example (slides 21-26)
  Launched from C2 helicopter ~5 seconds apart
  Each given unique random trajectory 30 seconds after initialization
    All agents given a 10 degree rate of climb
Define 8 target flyovers
  Command flyovers to swarm 120 seconds after 1st drone initialization
  Target flyovers defined on next slide

## Slide 33: Target Assignments – Example, Continued
Weights used in assignment:
    : 10
    : 1
    : 0.1
    : 100
    Assumptions:
      Distance from target is more important than altitude change required
      Velocity change required is not very important because FANGS will speed each aircraft up before intercept
      Heading change is very important because turning induces instability and costs a lot of flight time

## Slide 34: Target Assignments – Example, Continued
Target | Latitude (Deg, North) | Longitude (Deg, West) | Altitude (MSL) | Groundspeed (knots)
1 | 36.530367 | 112.057600 | 11000 | 50
2 | 36.179491 | 111.951595 | 12000 | 50
3 | 36.276756 | 112.687766 | 9600 | 50
4 | 36.542782 | 112.124202 | 12000 | 50
5 | 36.089355 | 112.409598 | 10000 | 50
6 | 36.218540 | 111.969167 | 12600 | 50
7 | 36.449291 | 112.399009 | 7700 | 50
8 | 36.580698 | 111.866192 | 9000 | 50
8 Flyover Assignments

## Slide 35: Target Assignments – Example, Continued
Agent | Latitude (Deg, North) | Longitude (Deg, West) | Altitude (MSL) | Groundspeed (knots) | Heading (Deg) | Flight Path Angle (Deg)
1 | 36.23111 | -112.27017 | 8525.751 | 80.058 | 182.888 | 10.00212
2 | 36.25135 | -112.24750 | 9046.887 | 106.007 | 99.566 | 10.00093
3 | 36.23797 | -112.29225 | 8535.040 | 96.050 | 268.649 | 10.01889
4 | 36.26619 | -112.28151 | 8425.689 | 80.023 | 1.920 | 9.999995
5 | 36.23514 | -112.27546 | 8424.269 | 102.037 | 208.198 | 10.02664
6 | 36.25800 | -112.26417 | 8195.515 | 94.866 | 82.316 | 10.00612
7 | 36.23767 | -112.28039 | 8077.037 | 84.689 | 225.048 | 10.03656
8 | 36.23940 | -112.28349 | 8047.320 | 90.942 | 245.432 | 10.07828
Agent States at 120 seconds (time of cost estimate)

## Slide 36: Target Assignments – Example, Continued
Agent-Target Cost Matrix with Optimal Assignments
Total assignment cost = 20784.93
 | AGENT 1 | AGENT 2 | AGENT 3 | AGENT 4 | AGENT 5 | AGENT 6 | AGENT 7 | AGENT 8
TARGET 1 | 2980.23 | 3798.31 | 1475.21 | 3988.04 | 1661.90 | 4399.78 | 1051.47 | 1049.03
TARGET 2 | 2298.85 | 3139.92 | 1106.01 | 3309.01 | 1307.57 | 3714.36 | 1401.93 | 447.31
TARGET 3 | 2923.33 | 3951.30 | 1302.78 | 3897.66 | 1685.80 | 4551.22 | 905.93 | 1038.87
TARGET 4 | 2852.11 | 3953.20 | 1558.17 | 3824.42 | 1980.81 | 4524.15 | 738.10 | 969.83
TARGET 5 | 3124.64 | 3947.58 | 1529.54 | 4108.66 | 1717.72 | 4548.34 | 929.64 | 1194.79
TARGET 6 | 3114.98 | 4031.45 | 1936.90 | 4123.21 | 2178.88 | 4601.87 | 719.90 | 1185.37
TARGET 7 | 3450.58 | 4324.94 | 1842.07 | 4425.55 | 2065.54 | 4925.22 | 636.43 | 1565.91
TARGET 8 | 3446.11 | 4392.38 | 1834.55 | 4420.77 | 2133.14 | 4992.35 | 578.07 | 1561.64

## Slide 37: Results

## Slide 38: Future Development - Agent Tracking
Each agent tracked by the C2
  Assumption: onboard radar, infrared, or other sensor system
Raw track data output by FANGS
  Target bearing, elevation, and range relative to C2
  Simulated sensor noise
    Gaussian noise
    Future iterations may simulate false tracks, track drop-outs, non-Gaussian noise, and range-dependent noise

## Slide 39: Future Development - Agent Tracking, Continued
Future Development: Implement random finite-set based tracking algorithms from University of Alabama LAGER Python package CARBS.
Add air-to-air targets and track these targets
  Intercept air-to-air targets with drones commanded by FANGS