## Slide 1: Tracking and Control of Air-Launched Fixed-Wing Autonomous Drone Swarm
Culminating Experience Project in the Pursuit of Mechanical Engineering Master’s Degree
Alex Springer, 2021 through 2024

## Slide 2: Project Definition and Overview
Air-Launched Drone Swarms
Independent Non-Linear Agent Control System
User-Specified Commands:
  Fly-Over Waypoints
  Drone trajectories
Agents Tracked by C2 Aircraft
Agents Autonomously Assigned to User Commands
Use-Case: Search and Rescue in Difficult Terrain
Note: Drones in the simulation are fixed-wing, not rotary-wing as shown

## Slide 3: Control System Hierarchy
Agent States Continuously Estimated
User Input of Fly-Over Waypoint (applications: search & rescue, surveillance, package drop)
Latitude, Longitude, Altitude, Groundspeed
Cost Estimated for Each Agent: Distance, Altitude, Heading, and Groundspeed all considered
Individual Agent Controller
Agent-Waypoint Assignment
Linear Hungarian Assignment Algorithm Used to Assign Agents and Minimize Overall Cost
Proportional Controller Converts Waypoint Assignments to Controller Inputs At Each Time Step
Non-Linear Navigation Controller to Command Airspeed, Heading, and Rate of Climb
Each Agent Tracked by Command & Control Aircraft
Agent Position, Velocity, and Acceleration Estimated by Random Finite-Set Based Filter
User Input

## Slide 4: Fixed-Wing Aircraft Non-Linear Guidance System (FANGS)
Individual Agent Flight Controller

## Slide 5: The Underlying Controller for Each UAS Agent
Based on Nonlinear Aircraft-Performance Simulation by Dr. John Schierman in his Modern Flight Dynamics textbook
Rigid fixed-wing aircraft operating in steady wind
Uses a default state estimator with ideal equations of motion
  User can provide a state solution at any time step; any unprovided state variables are estimated using the default ideal estimator
Input: desired flight profile
  Velocity, rate of climb, and heading

## Slide 6: Simulation Setup
Drones modelled loosely from a C-130 fixed-wing aircraft
  Long flight-time and/or range
  Heavy payload (cameras, telemetry, first-aid package drop, etc.)
Each drone launched from a C2 helicopter
Flight controller in operation 150 feet after launch
  Assume wings deploy during first 150 feet
  After 150 feet, assumed 50 kts airspeed with no ascent or descent
8 drones launched ~5 seconds apart

## Slide 7: Ideal EOM: Governing Equations
Translational equations of motion for a vehicle with propulsive thrust aligned with the fuselage x-axis:

## Slide 8: Ideal EOM: Simplifying Assumptions
Steady level flight or coordinated turns (sideslip and side force are zero)
Assume sufficiently small angles of attack such that
The governing equations become

## Slide 9: Ideal EOM: Engine and Airframe Responses
First-Order Differential Equations Used to Approximate the Engine and Airframe Responses
Limits imposed on the responses
Time constants , , set to 2.0, 0.5, and 1.0, respectively, in simulation

## Slide 10: Ideal EOM: Aerodynamic Responses
The model used in the ideal equations of motion for aerodynamic lift and drag
where, , , and
Note: FANGS is designed to operate within the presence of wind, where

## Slide 11: Ideal EOM: Angle of Attack and Drag
Invert the prior equations to find the inferred Angle of Attack and Drag given a Lift command
where , , and

## Slide 12: Guidance Laws – Transfer Functions
Inputs: Commanded Velocity , Rate of Climb , and Heading
Outputs: Commanded Thrust , Lift , and Bank Angle

## Slide 13: Guidance Laws - ODEs
Convert the transfer functions to ODEs to be programmed in Python 3 and solved using scipy.integrate.solve_ivp with the RK45 method:
where , , and

## Slide 14: Implementation (Python 3)
FANGS.py
  Create an object of class GuidanceSystem
    Initialization inputs:
      vehicle: Object of type FixedWingVehicle
      TF_constants: Dictionary of PI Controller transfer function coefficients ()
      InitialConditions: Dictionary of initial conditions
    User-Accessible Functions:
      setCommandTrajectory()
      setFlyoverCommand()
      getGuidanceCommands()
      updateSystemState()

## Slide 15: Implementation (Python 3), continued
After initialization, the drone is commanded to fly at initial conditions.
The user may give any drone a command of either:
  Trajectory
    The user will supply a desired airspeed, heading, and rate of climb.
  Flyover
    The user will supply a desired waypoint, altitude, and groundspeed.
Alternatively, the user may give the swarm a list of Flyover commands
  See ATAMS section for more.

## Slide 16: User Commands: Trajectory
User may request a trajectory command at any time:
  Velocity , Rate of Climb , and Heading
  Use setCommandTrajectory()
Guidance Laws calculated when getGuidanceCommands() is called
  Run this each time step
Use-Case: Loiter, Send-To-Home

## Slide 17: User Commands: Flyover
The user may request a flyover command at any time:
  Groundspeed (feet/sec), Altitude (ft, MSL), Waypoint (latitude, longitude)
  Use setCommandFlyover()
An internal flag will note that a flyover has been requested
At each timestep, when getGuidanceCommands() is run, FANGS will internally convert flyover commands to trajectory commands for the aircraft guidance logic
  Proportional Controller: see next slide

## Slide 18: User Commands: Flyover, continued
Correct aircraft altitude before adjusting velocity
  Calculate required glideslope to reach command altitude
    if :
    elseif :
    else:

## Slide 19: User Commands: Flyover, continued
Once altitude is stabilized, fly as fast as possible until within 1 mile of the flyover point
if :
    if distance from target 1 mile:
    velocity = maximum allowable velocity - 15
    else:
    velocity =

## Slide 20: User Commands: Flyover, continued
While changing velocity and altitude, continually adjust heading to intercept flyover point
    heading = bearing between(current latitude/longitude, target latitude/longitude)
If the aircraft is within 300 feet of the target, “let go” of the flyover waypoint and switch to a trajectory controller holding the current flight path for intercept.
  Aircraft will maintain this flight path until the user specifies a new trajectory or flyover command

## Slide 21: Example Simulation – Single Agent
Initial Conditions
  Airspeed = 50 knots
  Altitude = 7000 feet above mean sea level
  Ascent = 0 degrees
  Heading = 0 degrees (North)
  (Latitude, Longitude) = (36.2434, -112.2822) degrees
  Weight = 80 pounds
  Wind = 15 knots east

## Slide 22: Example Simulation – Single Agent
Drone Parameters
  Max speed = 75 knots
  Min speed = 25 knots
  = (2.0, 0.5, 1.0)
  Max thrust = 45 pounds
  Max = 0.26
  Max bank angle = 45 degrees
  = 0.05
  = 0.5 radians
  = -0.1 degrees
  Wing area = 8 square feet
  Aspect ratio = 12
  Wing efficiency factor = 0.8

## Slide 23: Example Simulation – Single Agent
Controller Transfer Function Gains

## Slide 24: Example Simulation – Inputs
After 120 seconds, command trajectory: 60 knots, 1 degree climb, West heading (270o)
After 360 seconds, command flyover: 50 knots, 4000 feet MSL, (36.530367, -112.057600)
Simulate 15 total minutes of flight time

## Slide 25: Example Simulation Results, Altitude
Dive commanded to aircraft to match flyover altitude

## Slide 26: Example Simulation Results, Airspeed
Drastic airspeed response due to dive (see previous slide)
After flyover, revert to northbound trajectory flight

## Slide 27: Agent Tracking and Assignment Management System (ATAMS)
Agent-Waypoint Assignment

## Slide 28: Target Assignments – Cost
Cost value assigned to each target-agent assignment
  Each calculation uses a weighting that can be user-defined
    : Weighting of Distance Cost
    : Weighting of Altitude Cost
    : Weighting of Velocity Cost
    : Weighting of Heading Cost
Calculate the cost of each possible agent-target assignment
  Ex: If 8 active agents and 4 assignments, 32 total cost calculations

## Slide 29: Target Assignments – Cost, Continued
Distance Cost:
  Simply multiply the distance between the agent and the target by
Heading Cost:
  Simply multiply the heading change required to intercept the target by
Altitude Cost:
  Multiply the required change in altitude by
  If the required altitude is lower than the current agent altitude, multiply the cost by 0.75
    Assumption: It is cheaper to lower an agent’s altitude than raise it
Velocity Cost:
  Simply multiply the velocity change required by
Total Assignment Cost: Sum the Distance, Heading, Altitude, and Velocity cost

## Slide 30: Target Assignments – Cost Matrix
Cost Matrix calculated using Hungarian Algorithm
  Use Python 3 scipy package scipy.optimize.linear_sum_assignment
  Returns cost matrix of n targets to m agents
Targets assigned by Cost Matrix

## Slide 31: Target Assignments - Example
Eight active airborne agents
  Each defined using parameters in Single Agent example (slides 21-26)
  Launched from C2 helicopter ~5 seconds apart
  Each given unique random trajectory 30 seconds after initialization
    All agents given a 10 degree rate of climb
Define 8 target flyovers
  Command flyovers to swarm 120 seconds after 1st drone initialization
  Target flyovers defined on next slide

## Slide 32: Target Assignments – Example, Continued
Target | Latitude (Deg, North) | Longitude (Deg, West) | Altitude (MSL) | Groundspeed (knots)
1 | 36.530367 | 112.057600 | 11000 | 50
2 | 36.179491 | 111.951595 | 12000 | 50
3 | 36.276756 | 112.687766 | 9600 | 50
4 | 36.542782 | 112.124202 | 12000 | 50
5 | 36.089355 | 112.409598 | 10000 | 50
6 | 36.218540 | 111.969167 | 12600 | 50
7 | 36.449291 | 112.399009 | 7700 | 50
8 | 36.580698 | 111.866192 | 9000 | 50
8 Flyover Assignments

## Slide 33: Target Assignments – Example, Continued
Agent | Latitude (Deg, North) | Longitude (Deg, West) | Altitude (MSL) | Groundspeed (knots) | Flight Path Angle (Deg) | Heading (Deg)
1 | 36.21510115 | -112.2566317 | 10381 | 133 | 10 | 184
2 | 36.25390053 | -112.2313545 | 9984 | 154 | 10 | 100
3 | 36.23337724 | -112.2970773 | 9206 | 137 | 10 | 269
4 | 36.26930124 | -112.2814132 | 8628 | 91 | 10 | 2
5 | 36.22838197 | -112.2728326 | 9074 | 147 | 10 | 209
6 | 36.26172295 | -112.25623 | 8719 | 135 | 10 | 82
7 | 36.22297227 | -112.2800674 | 9447 | 185 | 10 | 228
8 | 36.23542706 | -112.2840884 | 8495 | 128 | 10 | 246
Agent States at 120 seconds (time of cost estimate)

## Slide 34: Target Assignments – Example, Continued
Agent-Target Cost Matrix with Optimal Assignments
 | AGENT 1 | AGENT 2 | AGENT 3 | AGENT 4 | AGENT 5 | AGENT 6 | AGENT 7 | AGENT 8
TARGET 1 | 1141.99 | 1945.13 | 1002.96 | 2151.26 | 483.63 | 2549.38 | 2457.99 | 1623.34
TARGET 2 | 1363.79 | 2201.58 | 853.71 | 2375.81 | 385.72 | 2771.10 | 2118.63 | 1149.75
TARGET 3 | 2259.89 | 3289.82 | 634.33 | 3234.38 | 817.61 | 3890.19 | 1416.05 | 735.08
TARGET 4 | 2649.48 | 3753.53 | 1357.74 | 3621.49 | 1782.06 | 4324.34 | 888.39 | 767.44
TARGET 5 | 2485.49 | 3303.62 | 886.92 | 3464.55 | 1071.53 | 3905.37 | 1425.35 | 684.08
TARGET 6 | 2592.58 | 3510.76 | 1423.31 | 3601.69 | 1665.64 | 4080.59 | 1119.88 | 661.82
TARGET 7 | 2092.62 | 2972.50 | 483.69 | 3068.84 | 663.72 | 3574.72 | 1681.51 | 989.19
TARGET 8 | 3002.51 | 3951.41 | 1390.14 | 3977.48 | 1577.06 | 4551.88 | 919.08 | 1117.71

## Slide 35: Target Assignment – Example Results